## Slide 1
SAINTGITS COLLEGE OF ENGINEERING
Department of Electronics & Communications Engineering
BJT THERMAL RUNAWAY
Fixed Bias vs Voltage Divider Bias
EDC Project | Academic Year 2025–26
Project Guide: Dr Vinodkumar Jacob
Ajil Reji — 06 • Geojin Mathew — 31 • Jeril Liju Philip — 38 Joshua Joseph Varghese — 41 • Meeval Varghese — 47
Simulation-based investigation using LTspice

## Slide 2
Introduction & Objectives
Why biasing stability matters in transistor circuits
2
BJT basics
A bipolar junction transistor controls collector current through base drive. Its operating point depends on bias and temperature.
Thermal sensitivity
Temperature affects parameters such as base–emitter voltage and leakage current, shifting collector current.
Why compare biasing?
A stable operating point helps electronic circuits remain predictable as temperature changes.
Project objectives
• Compare fixed-bias and voltage-divider-bias circuits using a nominal 12 V supply. • Observe collector-current variation across a simulated temperature sweep. • Quantify the current change between 25°C and 80°C. • Discuss which bias arrangement provides better temperature stability in this simulation.
Scope: LTspice simulation only; no physical prototype has been tested.

## Slide 3
Thermal Runaway — Feedback Mechanism
Temperature sensitivity can contribute to instability under some conditions
3
1
Temperature rises
2
Collector current may rise
3
Power dissipation increases
4
Further heating may occur
Relevant relation
Approximate transistor power dissipation: P ≈ VCE × IC. Higher current can increase heating depending on operating conditions.
Important distinction
A current rise over a temperature sweep shows temperature sensitivity; it does not by itself prove thermal runaway occurred.
This project compares how two bias networks respond to temperature.

## Slide 4
Circuit Comparison
Component values taken from the supplied LTspice schematic
4
Key difference: the voltage-divider sets the base voltage; RE = 470 Ω provides negative feedback that tends to oppose current increases.

## Slide 5
LTspice Simulation Method
Both circuits were simulated in one file and swept over temperature
5
Software & model
LTspice • schematic label: 2N2222
Supply voltage
12 V for each circuit
Temperature sweep
.dc temp 25 150 1 25°C to 150°C in 1°C steps
Traces: I(Rc1) = fixed bias I(Rc2) = voltage-divider bias

## Slide 6
Simulation Results
Collector current at 25°C and 80°C
6
Parameter | Fixed bias | Voltage-divider
IC at 25°C | 9.957 mA | 6.0033 mA
IC at 80°C | 11.785 mA | 6.2812 mA
Absolute increase | 1.828 mA | 0.2779 mA
Percentage increase | 18.36% | 4.63%
Fixed bias
Current increase: 1.828 mA (18.36%)
Voltage-divider bias
Current increase: 0.2779 mA (4.63%)
Percent increase = (IC at 80°C − IC at 25°C) / IC at 25°C × 100

## Slide 7
Comparison & Discussion
Voltage-divider bias showed lower current variation in this simulation
7
Chart: Collector current by circuit and temperature
| Fixed bias | Voltage-divider
25°C | 9.957 | 6.0033
80°C | 11.785 | 6.2812
Fixed bias
18.36% increase from 25°C to 80°C
Voltage-divider bias
4.63% increase over the same interval
Fixed-bias percentage increase ≈ 3.96× the voltage-divider result.
The emitter resistor provides negative feedback. This supports a relative-stability conclusion, not proof of runaway.

## Slide 8
Sustainable Development Goals
Indirect relevance to reliable and responsible electronics design
8
SDG 9 — Industry, Innovation and Infrastructure
The project applies simulation to compare circuit design choices and understand stability in electronic systems. Better-informed design can support reliable engineering.
SDG 12 — Responsible Consumption and Production
Understanding thermal stress and stability can inform component protection and potentially reduce premature failure and electronic waste.
These are potential, indirect contributions; the project does not directly measure sustainability outcomes.

## Slide 9
Conclusion & Future Scope
What the simulation supports — and what remains to be tested
9
Conclusion
• Fixed bias: 18.36% collector-current increase • Voltage-divider bias: 4.63% increase • Voltage-divider bias showed lower current variation over 25–80°C.
Project limitation
Simulation only. No physical circuit was assembled, and thermal runaway was not experimentally demonstrated.
Future scope
• Assemble both circuits and measure collector current and transistor temperature. • Test additional temperatures and operating conditions. • Investigate thermal protection, heatsinking and component limits.
Main takeaway: emitter-resistor feedback improved temperature stability in this simulated comparison.

## Slide 10
REFERENCES
1. onsemi, 2N2222A / PN2222A NPN transistor datasheet. Verify the exact model variant used in LTspice.
2. Analog Devices, LTspice simulator resources: https://www.analog.com/en/resources/design-tools-and-calculators/ltspice-simulator.html
3. Sedra, A. S. and Smith, K. C., Microelectronic Circuits, Oxford University Press. BJT biasing and thermal stability theory.
4. United Nations, Sustainable Development Goals: https://sdgs.un.org/goals
5. Project data: LTspice schematic, temperature sweep graph and cursor readings supplied by the project team.
THANK YOU
Questions?
EDC Project • Saintgits College of Engineering